# Poco CAN bus Protocol DRAFT
Document Version	Date	Author	Changes
0.1	11/27/24	Paul Abbott	Initial Draft WIP
0.2	02/13/25	Paul Abbott	Updated NMEA2000 Manufacturer Code 1512 as issued for Lumitec. Describe changing instance number for Poco Switches Level 1.

Poco offers a few levels of CAN bus protocols to support a range of client capabilities and use-cases. The simple protocols can be implemented with single (8-byte) CAN frames. The higher level protocol requires multi-packet frames using either ISO-TP or N2K Fast-Packet method.
It is not recommended to use more than one protocol level in a particular application. The higher level protocols typically implement a super-set of the lower level's functions.
## Device Discovery
Poco supports the ISO address claim (PGN 60928). Poco will try to claim the address specified in the Poco configuration menu. If there is an address conflict on the CAN bus, Poco may assume another address and will save it to it's configuration. For robust discovery, clients should request and listen for PGN 60928 to identify Poco devices by NAME fields 2, 5, 7, and 9. NAME is defined as the contents of transmitted PGN 60928:
### Transmitted PGN 60928 (0xEE00) - ISO Address Claim (NAME)
Field #	Field Name	Description	Unit	Type	Byte #
1	Unique Number	Device Serial Number	0 .. 2097149	21 bits unsigned NUMBER	0,1,2
2	Manufacturer Code	1512: Lumitec		11 bits MANUFACTURER_CODE	2,3
3	Device Instance Lower		0 .. 6	3 bits unsigned NUMBER	4
4	Device Instance Upper		0 .. 29	5 bits unsigned NUMBER	4
5	Device Function	130: Lighting Controller	0 .. 253	8 bits unsigned NUMBER	5
6	Spare			1 bits SPARE	6
7	Device Class	126: Lighting	0 .. 125	7 bits lookup DEVICE_CLASS	6
8	System Instance		0 .. 13	4 bits unsigned NUMBER	7
9	Industry Group	4: Marine Industry	0 .. 6	3 bits lookup INDUSTRY_CODE	7
10	Arbitrary address capable		0 .. 1	1 bits unsigned NUMBER	7

## Poco Switches Level 1 – Poco ExtSw Binary (On/Off)
This protocol allows simple on/off switch control and status integration with many systems that already support the commonly-used standard "Binary Switch Bank Status" PGN 127501.
It uses single (8-byte) CAN frames. This PGN is not addressable (global), but it offers Bank / Instance to accommodate multiple Poco units. Poco External Switches are indexed by ID number: 1 ~ 28 in bank [i] and 29 ~ 32 in bank [i+1]. The base instance [i] can be changed via the Poco user interface or via the standard NMEA2000 method.
Limitations of this protocol level:
- No support for client to read text names of switches.
- No support for client to command actions other than On or Off.
- Switch state status is limited to only 3 values: 0: Off, 1: On, 3: Unavailable.
### Transmitted PGN 127501 (0x1F20D) - Binary Switch Bank Status
Poco periodically sends the binary state of each configured External Switch using this common standard "Binary Switch Bank Status" PGN 127501.
This single-frame PGN is 8 bytes long and contains 29 fields. It is transmitted every 2500 milliseconds, or when the state changes. The default priority is 3.
Field #	Field Name	Description	Unit	Type	Byte #
1	Bank / Instance	[i]: Switches 1 ~ 28 [i+1]: Switches 29 ~ 32 / (i is configurable, default=1)	0 .. 253	8 bits unsigned NUMBER	0
2	Switch 1 Status	0: Off, 1: On, 3: Unavailable	0 .. 2	2 bits lookup OFF_ON	1
3 ~ 29	Switch 2~28 Status	repeated 27 times	0 .. 2	2 bits lookup OFF_ON	1 ~ 7

### Received PGN 127502 (0x1F20E) - Binary Switch Bank Control
Poco reacts to requests to change the state of its External Switches this common standard "Binary Switch Bank Control" PGN 127502.
Note: Poco also reacts to the "Command Group Function" (PGN 126208) method to control the switch states by commanding a change to a field in PGN 127501.
This single-frame PGN is 8 bytes long and contains 29 fields.
Field #	Field Name	Description	Unit	Type	Byte #
1	Bank / Instance	[i]: Switches 1 ~ 28 [i+1]: Switches 29 ~ 32 / (i is configurable, default: i=1)	0 .. 253	8 bits unsigned NUMBER	0
2	Switch 1 Command	0: Turn Off, 1: Turn On, 3: No Change	0 .. 2	2 bits lookup OFF_ON	1
3 ~ 29	Switch 2~28 Command	repeated 27 times	0 .. 2	2 bits lookup OFF_ON	1 ~ 7

## Poco Switches Level 2 – Poco ExtSw Actions
This protocol is simple and efficient for use on small CAN networks where the client already knows about the Poco External Switches that it will query and control. It uses single (8-byte) CAN frames. It is addressed, so it can accommodate multiple Poco units.
Limitations of this protocol level:
- Poco External Switches are identified only by ID number 1 ~ 32.
- No support for client to read text names of switches or actions.
### Received PGN 61184 (0xEF00) – PID 1: External Switch: Simple Actions (no action parameters)
This PGN description applies when the following field(s) match:
Manufacturer Code	1512: Lumitec
Industry Code	4: Marine
Proprietary ID	1: External Switch: Simple Actions

The Action ID parameter must equal one of:
Action ID	0: no action (just return state of switch) / 1: "Off" (Sets Bright=0), / 2: "On" (Sets default Hue, default Sat, default Bright), / 3: "DimDn" (Bright -10%), / 4: "DimUp" (Bright +10%), / 6: "PStart" (Pattern Start *) / 7: "PPause" Pause/Resume Pattern), / 8: "T2HSB" (Default Hue, Sat, and Bright, Same as “On”) / 9: "T2HS" (Default Hue and Sat, *) / 10: "T2B" (Default Bright, no change to color) / 20: "Wht" (Change Color to White, *), / 21: "Red" (Change Color to Red, *), / 22: "Grn" (Change Color to Green, *), / 23: "Blu" (Change Color to Blue, *), / 31: "PlayPause" (Toggle Pattern Play/Pause), / 32: "Toggle" (Toggle On/Off and Scene Select advance), / 33~65: "On[n]" (Choose Scene Select child switch),

 * Several actions behavior depends on the previous state of the switch: If previous switch state was off, then also set default Brightness, else no change to Brightness.
This Manufacturer Proprietary Single-Frame Addressable PGN contains the following fields:
Field #	Field Name	Description	Unit	Type	Byte #
1	Manufacturer Code	1512: Lumitec		11 bits lookup MANUFACTURER_CODE	0~1
2	Reserved	Always 0b11		2 bits RESERVED	1
3	Industry Code	4: Marine Industry		3 bits lookup INDUSTRY_CODE	1
4	Proprietary ID	1: External Switch: Simple Actions	0 .. 253	8 bits unsigned NUMBER	2
5	Action ID	Action ID# see list above	0 .. 253	8 bits unsigned NUMBER	3
6	Switch ID	Switch ID#	0 .. 253	8 bits unsigned NUMBER	4
7		Unused		RESERVED	5~7

### Received PGN 61184 (0xEF00) – PID 3: External Switch: Custom Hue, Saturation, Brightness
This PGN description applies when the following field(s) match:
Manufacturer Code	1512: Lumitec
Industry Code	4: Marine
Proprietary ID	3: External Switch: Custom Hue,Sat,Bright
Action ID	8: "T2HSB" (Custom Hue, Sat, and Bright) / 9: "T2HS" (Custom Hue and Sat, *) / 10: "T2B" (Custom Bright, no change to color)

 * T2HS action behavior depends on the previous state of the switch: If previous switch state was off, then also set default Brightness, else no change to Brightness.
This Manufacturer Proprietary Single-Frame Addressable PGN contains the following fields:
Field #	Field Name	Description	Unit	Type	Byte #
1	Manufacturer Code	1512: Lumitec		11 bits MANUFACTURER_CODE	0~1
2	Reserved	Always 0b11		2 bits RESERVED	1
3	Industry Code	4: Marine Industry		3 bits lookup INDUSTRY_CODE	1
4	Proprietary ID	3: External Switch: Custom Hue,Sat,Bright	0 .. 253	8 bits unsigned NUMBER	2
5	Action ID	Action ID# / 8: "T2HSB" (Custom Hue, Sat, and Bright) / 9: "T2HS" (Custom Hue and Sat, *) / 10: "T2B" (Custom Bright, no change to color)	0 .. 253	8 bits unsigned NUMBER	3
6	Switch ID	Switch ID#	0 .. 253	8 bits unsigned NUMBER	4
7	Hue	Custom Hue value / (0:Red, 85: Green, 170: Blue / 255: close to Red)	0 .. 255	8 bits USING FULL RANGE 0~255	5
8	Saturation	Custom Color Saturation Value / 0: White, 16: Fully saturated color. / (Note: scaled-down internally to capable resolution T2HSB:3b, T2HS:4b)	0 .. 255	8 bits USING FULL RANGE 0~255	6
9	Brightness Abs	Custom Brightness (absolute value) 0: Off, 255: Fully On / (Note: scaled-down internally to capable resolution T2HSB:4b,T2B:8b)	0 .. 255	8 bits USING FULL RANGE 0~255	7

### Received PGN 61184 (0xEF00) – PID 4: External Switch: 6: Start Pattern ID
This PGN description applies when the following field(s) match:
Manufacturer Code	1512: Lumitec
Industry Code	4: Marine
Proprietary ID	4: External Switch: Start Pattern ID

 * Pattern Start action behavior depends on the previous state of the switch: If previous switch state was off, then also set default Brightness, else no change to Brightness.
This Manufacturer Proprietary Single-Frame Addressable PGN contains the following fields:
Field #	Field Name	Description	Unit	Type	Byte #
1	Manufacturer Code	1512: Lumitec		11 bits MANUFACTURER_CODE	0~1
2	Reserved	Always 0b11		2 bits RESERVED	1
3	Industry Code	4: Marine Industry		3 bits lookup INDUSTRY_CODE	1
4	Proprietary ID	4: External Switch: Start Pattern ID	0 .. 253	8 bits unsigned NUMBER	2
5	Switch ID	Switch ID#	0 .. 253	8 bits unsigned NUMBER	3
6	Pattern ID	ID# of pattern	0 .. 255	8 bits unsigned NUMBER	4
		Unused		RESERVED	5~7

TODO:
5: "T2BD" (Custom Delta Bright, no change to color),
RGB actions?
### Transmitted PGN 61184 (0xEF00) – PID 2: External Switch: Switch State Information
This PGN description applies when the following field(s) match:
Manufacturer Code	1512: Lumitec
Industry Code	4: Marine
Proprietary ID	2: ExtSw API State

This Manufacturer Proprietary Single-Frame Addressable PGN contains the following fields: By default it is transmitted every 2500 milliseconds for each configured Switch, or when the state changes. The default priority is ??
Field #	Field Name	Description	Unit	Type	Byte #
1	Manufacturer Code	1512: Lumitec		11 bits MANUFACTURER_CODE	0~1
2	Reserved	Always 0b11		2 bits RESERVED	1
3	Industry Code	4: Marine Industry		3 bits lookup INDUSTRY_CODE	1
4	Proprietary ID	2: ExtSw API State	0 .. 253	8 bits unsigned NUMBER	2
5	ExtSw ID	Switch ID#	0 .. 253	8 bits unsigned NUMBER	3
6	ExtSw State	Combined state variable / 0: OFF, other: ON (brightness)	0 .. 255	8 bits USING FULL RANGE 0~255	4
7	ExtSw Type (mode?)	253: Not Configured / 0: Off / 1: Hue / Saturation / 2. White Kelvin Temp (reserved for future use) / 3. Running Pattern/Fx / 4. Scene Select (Mutex)	0 .. 253	8 bits unsigned NUMBER	5
	Hue / Sat	?			6
	Pattern/Fx ID#	?			7

* Combined State variable is interpreted based on type of switch:

## Poco Switches Level 3 – Standard N2K Lighting System
All capabilities of Protocol Level 2 and 1, plus:
Enumeration of switches, names, types, actions
Makes use of N2K Command Group Function (PGN 126208) to change states.
Makes use of (a subset) of new N2K standard “Lighting” PGNs:
  - PGN 130330 - Lighting System Settings
  - PGN 130561 - Lighting Zone
## Poco Output Channel
At this protocol level, Poco is just a conduit that sets output channels as commanded with PLI, PWM, BIN commands.
Poco does not keep track of virtual switch logic or the states of lights at this level. It only reports the status of the output channel.
### Transmitted PGN 61184 (0xEF00) – PID 5: Poco Output Channel: Status
This PGN description applies when the following field(s) match:
Manufacturer Code	1512: Lumitec
Industry Code	4: Marine
Proprietary ID	5: Poco Output Channel: Status

This Manufacturer Proprietary Single-Frame Addressable PGN contains the following fields: By default it is transmitted every 2500 milliseconds, or when the state changes. The default priority is ??
Field #	Field Name	Description	Unit	Type	Byte #
1	Manufacturer Code	1512: Lumitec		11 bits MANUFACTURER_CODE	0~1
2	Reserved	Always 0b11		2 bits RESERVED	1
3	Industry Code	4: Marine Industry		3 bits lookup INDUSTRY_CODE	1
4	Proprietary ID	5: Poco Output Channel: Status	0 .. 253	8 bits unsigned NUMBER	2
5	Channel	1 ~ 4 Poco output channel #	0 .. 253	8 bits unsigned NUMBER	3
6	Channel Mode	0: None (Off) / 1: BIN (On/Off only) / 2: PWM (Dimming) / 3: PLI (Power Line Instruction)	0 .. 253	8 bits unsigned NUMBER	4
7	Channel Output Level	Channel output level (commanded, not measured) / 0: Low (Channel Off) / 1: High (Channel On) / If PWM mode: 0~255 (Duty)	0 .. 255	8 bits FULL_RANGE 0~255	5
8	Channel Input Voltage	(measured at channel input, useful to indicate blown fuse) / (0 ~ 50,600 mV)	200 mV	8 bits unsigned NUMBER	6
9	Channel Current	(0 ~ 25,300 mA)	100 mA	8 bits unsigned NUMBER	7

### Received PGN 61184 (0xEF00) – PID 16: Poco Output Channel: PLI T2HSB
This PGN description applies when the following field(s) match:
Manufacturer Code	1512: Lumitec
Industry Code	4: Marine
Proprietary ID	16: Poco Output Channel: PLI T2HSB

This is a convenience PGN that formats the supplied parameters into a PLI message and sends it on the specified Poco Output Channel. The effect is equivalent to supplying the raw PLI message to PGN: 6: Poco Output Channel: PLI Raw.
This Manufacturer Proprietary Single-Frame Addressable PGN contains the following fields:
Field #	Field Name	Description	Unit	Type	Byte #
1	Manufacturer Code	1512: Lumitec		11 bits MANUFACTURER_CODE	0~1
2	Reserved	Always 0b11		2 bits RESERVED	1
3	Industry Code	4: Marine Industry		3 bits lookup INDUSTRY_CODE	1
4	Proprietary ID	16: Poco Output Channel: PLI T2HSB	0 .. 253	8 bits unsigned NUMBER	2
5	Channel	1 ~ 4 Poco output channel #	0 .. 253	8 bits unsigned NUMBER	3
	PLI Clan	PLI Address/Clan (0: All, 1~63: see table xx)	0 .. 63	6 bits FULL_RANGE 0~63	4
	Transition	Transition Time ID (see table xx)	0 .. 7	3 bits FULL_RANGE 0~7	4,5
	Brightness	Brightness Value (0: Off ~ 15: Full Bright)	0 .. 15	4 bits FULL_RANGE 0~15	5
	Hue	Hue value / (0:Red, 85: Green, 170: Blue / 255: close to Red)	0 .. 255	8 bits FULL_RANGE 0~255	6
	Saturation	Custom Color Saturation Value / 0: White ~ 7: Fully saturated color.	0 .. 7	3 bits FULL_RANGE 0~7	7
		TODO: add padding bits to align some fields to bytes

### TODO more convenience PGNs
T2RGB Transition to RGB (single message) (not absolute color-space)
T2HS Transition to new Hue and Sat
T2B Transition to Brightness (no change in Hue) (Unit: 0.39% = 1/255)
T2BD Transition Brightness by Delta (Unit: +/- 0.79% = 1/127)
T2P Transition to Pattern (see pattern table)

### Received PGN 61184 (0xEF00) – PID 8: Poco Output Channel: PLI Message
This PGN description applies when the following field(s) match:
Manufacturer Code	1512: Lumitec
Industry Code	4: Marine
Proprietary ID	8: Poco Output Channel: PLI Message

This Manufacturer Proprietary Single-Frame Addressable PGN contains the following fields:
Field #	Field Name	Description	Unit	Type	Byte #
1	Manufacturer Code	1512: Lumitec		11 bits MANUFACTURER_CODE	0~1
2	Reserved	Always 0b11		2 bits RESERVED	1
3	Industry Code	4: Marine Industry		3 bits lookup INDUSTRY_CODE	1
4	Proprietary ID	8: Poco Direct – PLI Message	0 .. 253	8 bits unsigned NUMBER	2
5	Channel	1 ~ 4 Poco output channel #	0 .. 253	8 bits unsigned NUMBER	3
6	PLI message	32bit PLI message		32 bits unsigned NUMBER	4~7

TODO: PLI channel config (timing, sync)
TODO: PLI channel power (set power on with start-inhibit / and power off)
### Received PGN 61184 (0xEF00) – PID 7: Poco Output Channel: PWM DUTY
This PGN description applies when the following field(s) match:
Manufacturer Code	1512: Lumitec
Industry Code	4: Marine
Proprietary ID	7: Poco Output Channel: PWM Dimming

This Manufacturer Proprietary Single-Frame Addressable PGN contains the following fields:
Field #	Field Name	Description	Unit	Type	Byte #
1	Manufacturer Code	1512: Lumitec		11 bits MANUFACTURER_CODE	0~1
2	Reserved	Always 0b11		2 bits RESERVED	1
3	Industry Code	4: Marine Industry		3 bits lookup INDUSTRY_CODE	1
4	Proprietary ID	7: Poco Output Channel: PWM Dimming	0 .. 253	8 bits unsigned NUMBER	2
5	Channel	1 ~ 4 Poco output channel #	0 .. 253	8 bits unsigned NUMBER	3
	Duty	PWM duty-cycle (dimming value)
	Transition	Time interval to transition (fade) to new duty-cycle

TODO: PWM channel config (set frequency, gamma, min-duty, default transition)
### Received PGN 61184 (0xEF00) – PID 6: Poco Output Channel: BIN On/Off
This PGN description applies when the following field(s) match:
Manufacturer Code	1512: Lumitec
Industry Code	4: Marine
Proprietary ID	6: Poco Output Channel: BIN On/Off

This Manufacturer Proprietary Single-Frame Addressable PGN contains the following fields:
Field #	Field Name	Description	Unit	Type	Byte #
1	Manufacturer Code	1512: Lumitec		11 bits MANUFACTURER_CODE	0~1
2	Reserved	Always 0b11		2 bits RESERVED	1
3	Industry Code	4: Marine Industry		3 bits lookup INDUSTRY_CODE	1
4	Proprietary ID	6: Poco Output Channel: BIN On/Off	0 .. 253	8 bits unsigned NUMBER	2
5	Channel	1 ~ 4 Poco output channel #	0 .. 253	8 bits unsigned NUMBER	3
	Duty	PWM duty-cycle (dimming value)
	Transition	Time interval to transition (fade) to new duty-cycle

## Misc. Utilities PGNs
### Received PGN 126720 (0x1EF00) – PID: ? Encapsulated Poco-Proto
Manufacturer Proprietary Fast-Packet Addressable
(Lumitec internal use only)